## Slide 1: Power supply
Vlad Veliciu

## Slide 2: Block diagram

## Slide 3: The rectifier
Functioning:
D1, D4 conduct on the positive alternance of Vin
D2, D3 on the negative alternance
C reduces the ripple

## Slide 4: The rectifier - design
Maximum voltage ripple of 1V

## Slide 5: The rectifier - components
Transformer: VPP20-1500
Diodes: 1N4001
URRm = 50V
Idmax = 30A
Iavg <1A
Capacitors: 7x EKYC250ELL202MK20S (2mF) and 1x 25ZLQ1800MEFC12.5X20 (1.8mF)

## Slide 6: The rectifier - simulation
Voltage ripple
IDmax
Output power

## Slide 7: Series voltage regulator

## Slide 8: Series voltage regulator - design
For the transistor:
For the Zener diode:
Chosen components:
BD135-16
BZX84C13VLY

## Slide 9: Series voltage regulator - design
Internal resistance Zener diode:
RZ=0.95Ω

## Slide 10: Series voltage regulator - design

## Slide 11: Series voltage regulator - simulations
Ro = 0.25Ω
Sui = 89.87

## Slide 12: Series voltage regulator - simulations
Pdmax = 1.7W
Pdavg = 1.48W

## Slide 13: Series voltage regulator – heatsink for transistor
→
507302B00000G
Rth = 24 °C/W

## Slide 14: IC voltage regulator
Yellow: Bandgap reference
Green: Start-up circuit
Purple: Protection circuits
Q16: controls current between
input and output
Orange: Amplifier
LM7805
Vin = 7.5V…20V
Vout = 4.75V…5.25V
Notes: Q16 – controls current between INPUT and OUTPUT and so the output voltage
Yellow – bandgap reference (keeps the voltage stable): error signal from bandgap fed to Q7 and the orange part (amplifier)
Amplified signal controls Q15 which itself controls Q16 -> feedback
Green part – start-up circuit (initial current for the bandgap)
Q13 – protection from overheat
Q19 – overvoltage protection from input
Q14 – overcurrent protection from output
Blue part (voltage divider), sets output voltage

## Slide 15: IC voltage regulator
Decoupling capacitors: filter out the noise
(high frequency and transient signals)
Diode: protects series pass transistor
Notes: Decoupling capacitors: at frequency of the noise they have very low impedance and drive the noisy components to GND
Capacitor at input: required if IC placed far from the rectifier
Capacitor at output: helps the transient response (reduces rise/fall times and overshoot)
Diode: prevents reverse biasing of the series pass transistor if the output voltage goes higher than the input one

## Slide 16: IC regulator - simulations
Sui = 2000000
Ro = 0.0008Ω

## Slide 17: DC-DC step-down Buck converter

## Slide 18: DC-DC step-down Buck converter
→

## Slide 19: DC-DC step-down Buck converter – inductor design
Chosen inductor: PA2729.443NL (44μH and maximum saturation current of 7.3A )

## Slide 20: DC-DC step-down Buck converter – transistor and diode design
Transistor:
Diode:
Chosen transistor: BSC093N04LS (VDSmax=40V and IDSmax=13A)
Chosen diode: B530C (Idavgmax=5A and Urmax=30V)

## Slide 21: DC-DC step-down Buck converter – capacitor design
Chosen capacitor: 50ZLJ560M12.5X20 (Umax=50V and IRMSmax=1.26A)

## Slide 22: DC-DC step-down Buck converter – simulations
Iout
Vout
IS

## Slide 23: DC-DC step-down Buck converter – simulations
UT (blue)
IT (blue)

## Slide 24: DC-DC step-down Buck converter – simulations
UD (blue)
ID (blue)

## Slide 25: DC-DC step-down Buck converter – simulations
UL
IL

## Slide 26: DC-DC step-down Buck converter – simulations
IC